## Slide 1: CIS 11 – Computer Architecture
James Wilson

## Slide 2: Discrete Math: Truth Tables
X | Y | AND | OR | NOT | XOR
0 | 0 | 0 | 0 | 1,1 | 0
0 | 1 | 0 | 1 | 1,0 | 1
1 | 0 | 0 | 1 | 0,1 | 1
1 | 1 | 1 | 1 | 0,0 | 0

## Slide 3: Logical Operators: AND
Performs a bit-wise AND on two operands
  reg,reg
  reg,mem
  reg,imm
  mem,reg
  mem,imm
  .data
  array BYTE 50 DUP(?)
  .code
  mov ecx,LENGTHOF array
  mov esi,OFFSET array
  L1:
  and BYTE PTR [esi],11011111b ; clear bit 5
  inc esi
  loop L1

## Slide 4: Logical Operators: OR
Performs a bit-wise OR on two operands
  reg,reg
  reg,mem
  reg,imm
  mem,reg
  mem,imm

## Slide 5: Logical Operators: XOR
Performs a bit-wise OR on two operands
  reg,reg
  reg,mem
  reg,imm
  mem,reg
  mem,imm

## Slide 6: Logical Operators: NOT
Performs a bit-wise NOT on an operand
  reg
  mem
  Essentially toggles each bit in an operand

## Slide 7: Conditional Branching
CMP
  Implied subtraction between two operands
  Results are discovered by checking various flag registers
IF statements
  We now have the basic tools we need to implement conditional branching (if statements)
  What are they?

## Slide 8: Conditional Branching
JCOND
  Conditional jump
  Jumps to a location if certain status flag conditions are true

## Slide 9: Conditional Branching
Equality checks

## Slide 10: Example 1
mov edx,-1
cmp edx,0
jnl L5 ; jump not taken (-1 >= 0 is false)
jnle L5 ; jump not taken (-1 > 0 is false)
jl L1 ; jump is taken (-1 < 0 is true)

## Slide 11: Example 2
mov bx,+32
cmp bx,-35
jng L5 ; jump not taken (+32 <= -35 is false)
jnge L5 ; jump not taken (+32 < -35 is false)
jge L1 ; jump is taken (+32 >= -35 is true)

## Slide 12: Example 3
mov al,+127 ; hexadecimal value is 7Fh
cmp al,-128 ; hexadecimal value is 80h
ja IsAbove ; ??
jg IsGreater ; ??

## Slide 13: Additional Concepts
Nested conditions
  Short Circuiting
While loops
  Book example page 212-213
White Box Testing
Control flow Directives